# Text boxes

Access all menu functions by pressing FW then SET, then dial #.

SHORTCUTS

These are shortcut buttons direct to some of the menu functions.

Press FW then key #

#1 = menu item #29 - sql type

#2 = menu item #30 - tone set

#3 = menu item #32 - DTMF

#4 = memory group set

#5 = menu item #16 - APO

#6 = menu item #7 - rptr shift

#7 = menu item #11 – VFO step

#8 = (none)

#9 = menu item #20 - key beep

#0 = menu item #1- sql level

MR = set memory skip

VFO = dual watch on/off

Tone Search Scanning

Set up for CTCSS/DCS oper.

T and SQ must be displayed

Press FW then 2(CD), press VFO(DW)SC to start scanning, press SET when scan stops to lock in tone, then PTT to exit.

TX PWR Level

HI: 	5W 	Hi

L|||	 1W 	L3

L|| 	. 5W	L2

L|	. 3W 	L1

Press TX PO for power level L1, L2 or L3. No icon = Hi

Supply Voltage & Current

Nominal:	7.2 vdc

Operating:	10 – 16 vdc

Standby :	55mA (saver off)

Standby :	25mA (saver on)

Max TX :	1.9 A

Memory offset Tuning

When in Memory Recall mode press MR to switch to Memory Tuning mode.  Tune up or down from present freq using  DIAL.

Memory Scanning

Press MR for 1 second in memory recall to start scanning.

VFO Scanning

Press VFO for 1 second in VFO mode to start scanning.

Microprocessor Reset

Press and hold 4(MG), MR and VFO while turning power on Set Mode Reset

Press and hold MR and VFO while turning power on. Then press FW to reinitialize Set mode.

Set Priority channel

Select channel, FW 1 sec. BAND

Smart Search

Auto stores freqs in selected band above/below current freq. 31 chnls available (15 above & 15 below plus current freq).  Single = one sweep in each direction.  Continuous = sweeps until all 31 channels filled.

Select search mode type with menu item #35. Select VFO in desired band. Press FW for 1 sec. then LAMP.  Press VFO to begin scan. Watch loading of memory ch on display. To recall rotate DIAL. Exit by pressing FW then LAMP. Spectrum Analyzer

As above except use menu item #34 to set, FW, LAMP to start, PTT, FW, LAMP to end.

Cloning

Press FW while turning on, display reads “CLONE” Press MR on destination radio, VFO on source radio.

Program memory Scan

Store lower freq L(1-10) store upper freq in matching U memory. Switch to MR mode, select L(x) memory. Press MR, use DIAL or VFO for 1 sec to scan.

Memory scan skip

Set to MR mode, select ch to skip. Press FW then MR to activate, displays “( ” symbol next to channel number.

Preferential scan list

Same as above except FW, MR twice, note symbol displayed. Start scan from this type ch.